The NEC IR transmission protocol uses pulse distance encoding of the message bits. Each pulse burst (mark – RC transmitter ON) is 562.5µs in length, at a carrier frequency of 38kHz (26.3µs). Logical bits are transmitted as follows:
Logical '0' – a 562.5µs pulse burst followed by a 562.5µs space, with a total transmit time of 1.125ms
Logical '1' – a 562.5µs pulse burst followed by a 1.6875ms space, with a total transmit time of 2.25ms

When a key is pressed on the remote controller, the message transmitted consists of the following, in order:
a 9ms leading pulse burst (16 times the pulse burst length used for a logical data bit)
a 4.5ms space
the 8-bit address for the receiving device
the 8-bit logical inverse of the address
the 8-bit command
the 8-bit logical inverse of the command
a final 562.5µs pulse burst to signify the end of message transmission.
The four bytes of data bits are each sent least significant bit first. Figure 1 illustrates the format of an NEC IR transmission frame, for an address of 00h (00000000b) and a command of ADh (10101101b).

Figure 1. Example message frame using the NEC IR transmission protocol.
Notice from Figure 1 that it takes:
27ms to transmit both the 16 bits for the address (address + inverse) and the 16 bits for the command (command + inverse). This comes from each of the 16 bit blocks ultimately containing eight '0's and eight '1's - giving (8 * 1.125ms) + (8 * 2.25ms).
67.5ms to fully transmit the message frame (discounting the final 562.5µs pulse burst that signifies the end of message).
## Repeat Codes
If the key on the remote controller is kept depressed, a repeat code will be issued, typically around 40ms after the pulse burst that signified the end of the message. A repeat code will continue to be sent out at 108ms intervals, until the key is finally released. The repeat code consists of the following, in order:
a 9ms leading pulse burst
a 2.25ms space
a 562.5µs pulse burst to mark the end of the space (and hence end of the transmitted repeat code).
Figure 2 illustrates the transmission of two repeat codes after an initial message frame is sent.

Figure 2. Example repeat codes sent for a key held down on the transmitting remote controller.